## Slide 1: Software Defined Networking: Introduction to SDN & OpenFlow
James Won-Ki Hong
Department of Computer Science and Engineering
POSTECH, Korea
jwkhong@postech.ac.kr

## Slide 2: Outline
Background
Software Defined Networking
OpenFlow

## Slide 3: Background
Needs for a New Networking Paradigm
  Changing Traffic Patterns
    Data Center Traffic
    North-south: 95%  East-west: 40 ~ 80%
  Data Center Networks
    Hyper scale network
      Hundreds and thousands of servers
      Hundreds and thousands of switches  Tera bit network capacity
      3-4 tier architecture  over 50% of network capacity is used to connect switches  inefficient
TOR
Access
Aggregation
Core Router

## Slide 4: Background
Need for a new Networking Paradigm
  Vendor dependency
    Lack of open I/F and standard API  operators cannot tailor the N/W
    Biz needs and user demand  standard  Long Time to Market
      Vendor’s equipment product cycle  over 3 years
  Fundamental problems of IP protocols
    Protocols defined in isolation, each to solve a specific problem and without the benefit of abstractions.
      ~ 6,776 RFCs
    Current Internet needs many new dedicated middleboxes
      Lack of IPv4 addresses (232)  NAT, IPv6 (2128)
      Security  IDS/IPS, VLAN, VPN
      Management  Authentication, QoS, ACL…
    Today’s Internet… static
      To add or delete any device, IT must touch multiple devices and configurations.
      But, human errors are common
Center Router
Core Router
GSR
GES
Metro SW
L3
L2
Server Farm
AAA
Mail
DNS
DDNS
F/W
MPLS
Multi- cast
VPN
IGP
IPv6
NAT
DHCP
VLAN
ACL
Abstraction
Application
Fn
Fn
Fn
Fn

## Slide 5: SDN Background
Rapid Development of OpenFlow Technologies
  2012 ONF meeting, Google announced that…
    Google’s G-Scale network is operating using OpenFlow
    Developed for 2 years (2010~2012.1)
    Saved CAPEX and OPEX
  OpenFlow was known as an open standard to test experimental protocols in the campus networks
  OpenFlow  now evolving to Enterprise and Carrier grade SDN technologies
    Commercial OpenFlow switches and controllers
    NEC, NTT Data, Nicira , HP, IBM, BigSwitch, Brocade……

## Slide 6: Traditional Network Node
Router
  Router can be partitioned into three planes
    Management plane  configuration
    Control plane  make decision for the route
    Data plane  data forwarding
Adjacent Router
Router
Management/Policy plane
Configuration / CLI / GUI
Static routes
Control plane
OSPF
Neighbor table
Link state database
IP routing table
Forwarding table
Data plane
Data plane
Control plane
OSPF
Adjacent Router
Data plane
Control plane
OSPF
Routing
Switching

## Slide 7: SDN Concept
SDN separates Control and Data plane functions
(source “Understanding L3 Switch”, Netmanias Talk, 2011/11/09)
Control & Management Plane
Data Plane
SDN Switch (H/W)
Router/Switch
SDN Controller
(S/W)
OpenFlow

## Slide 8: SDN Concept
SDN Concept
  Separates control plane and data plane entities
    Network intelligence and state are logically centralized
    The underlying network infrastructure is abstracted from the applications
  Execute or run control plane software on general purpose hardware
    De-couple from specific networking hardware
    Use commodity computers
  Have programmable data planes
    Maintain, control and program data plane state from a central entity
  An architecture to control not only a networking device but an entire network
    Similar to existing Network Management System (NMS), but more powerful
Control Software (SW)
  Control SW operates on view of network
  Control SW is not a distributed system
    Abstraction hides details of distributed states

## Slide 9: SDN with Key Abstraction in the Control Plane
Network Operating System
Routing
Traffic Engineering
Other Applications
Well-defined API
Network Map
Abstraction
Forwarding
Forwarding
Forwarding
Forwarding
Network Virtualization

## Slide 10: SDN vs. OpenFlow
ONF Definition
  SDN performs Software Defined Forwarding
    Controls data forwarding through open API
  SDN provides Management Abstraction
    Can make more advance applications
Currently implemented with OpenFlow
OpenFlow is misunderstood to be equivalent to SDN
  No requirement for the use of OpenFlow within an SDN
  OpenFlow is one of SDN protocols but most popular as of Mar. 2015
Logical View of SDN architecture
Simplify
Vendor independent control…
Version | Date | Characteristics | Organization
OpenFlow 1.0 | 2009.12 | MAC, IPv4, single flow table | OpenFlow Consortium
OpenFlow 1.1 | 2011.2 | MPLS/tunnel, multiple flow tables, group table | OpenFlow Consortium
OpenFlow 1.2 | 2011.12 | IPv6, Config., extensible match support | ONF
OpenFlow 1.3 | 2012.9 | QoS (meter table)… | ONF
OpenFlow 1.4 | 2013.10 | Optical port monitoring and config (frequency, power) | ONF
OpenFlow 1.5 | 2014.12 | Egress table, pkt. type aware pipeline, flow entry stat trigger | ONF
Notes: OpenFlow 1.5
Egress table: In previous versions of the specification, all processing was done in the context of the input port.
Version 1.5 introduces Egress Tables, enabling processing to be done in the context of the output port
(EXT-306). When a packet is output to a port, it will start processing at the first egress table where
flow entries can define processing and redirect the packet to other egress tables.
Packet Type Aware Pipeline: In previous versions of the specification, all packets must be Ethernet packets. Version 1.5 introduces a packet aware pipeline, enabling processing of other types of packets, such as IP packets or PPP packets (EXT-112). A new OXM pipeline field identifies the packet type. The packet type is defined in an extensible manner, it uses multiple namespaces defined by other standard and allow experimenter packet types.
Flow Entry Statistic Trigger: Polling flow entry statistics can induce high overhead and utilization for the switch. A new statistics trigger mechanism enable statistics to be automatically sent to the controller based on various statistics thresholds.

## Slide 11: OpenFlow
Definition
  A communication protocol that gives access to the forwarding plane of the network switch or router
Features
  OpenFlow is similar to an x86 instruction set for the network
  Separation of control plane and data plane
    The data path of an OpenFlow switch consists of a Flow Table, and an action associated with each flow entry
    The control path consists of a controller which programs flow entry in the flow table
  OpenFlow is based on an Ethernet switch, with an internal flow-table, and a standardized interface to add and remove flow entries
Components
  OpenFlow controller
    Process packet match, instruction & action set, pipeline processing
  OpenFlow switch
    Secure channel, flow table

## Slide 12: OpenFlow History
USA NSF FIND (Future INternet Design) Program
  2006, Stanford and Berkley Univ.
  SANE(clean-slate Security Architecture for Enterprise Network) project
  Ethane project
    MS and Ph.D thesis
OpenFlow
  2007, Stanford Univ.
  2008, OpenFlow Consortium
  2008, Nicira Networks released NOX platform.
  2009, OpenFlow Spec 1.0
  2009 MIT Tech. Review  SDN as one of 10 emerging technologies
  2011 March, ONF (Open Networking Foundation) was born
  Facebook, Google, Microsoft, Yahoo  Data Center Operators
  Expand OpenFlow technologies to SDN
  2012 ONF released OpenFlow 1.3
  2013 ONF released OpenFlow 1.4
  Dec. 19th, 2014, ONF released OpenFlow 1.5

## Slide 13: How Does OpenFlow Work?
OpenFlow Switch and Tables
General purpose PC, Server
OpenFlow
protocol
Data Path, H/W
Control Path
OpenFlow
Controller (Server Software)
App
App
App
Ethernet Switch

## Slide 14: Current Status of SDN Products and Solutions
Vendors
  NEC: released OpenFlow 1.3 switch and controller… 2013.9
  HP: released OpenFlow 1.3 data center switch … 2013
  Centec Network, China: released Open SDN switch with OpenFlow1.3 support (implemented on OpenVswitch) … 2013.4
  Brocade, OpenFlow 1.3 switch … 2014.6~
 | Solutions | OpenFlow version | 
Controller | NOX | Support OpenFlow 1.3 | C++ API
 | POX | Python version of NOX, Support OpenFlow 1.1 | Python API
 | Floodlight | Support OpenFlow 1.3 | BigSwitch joined OpenDaylight but left it on June 2013
 | Ryu | Support OpenFlow 1.4 | Python API
 | OpenDayLight (ODL) | Support OpenFlow 1.3 | 2014.2
Switch | Open vSwitch | Support OpenFlow 1.3 | 
 | Ericsson soft switch | Support OpenFlow 1.3 | Compatible with Mininet Controller: NOX 1.3
Open Source

## Slide 15: OpenFlow Protocol Format
Protocol Layer
  OpenFlow control message relies on TCP protocol
  Controllers listen on TCP port 6633/6653 to setup conn. with switch
    6633/6653 became the official IANA port since 2013-07-18
  OpenFlow message structure
    Version
      Indicates the version of OpenFlow which this message belongs
    Type
      Indicates what type of message is present and how to interpret the payload (version dependent)
    Message length
      Indicates where this message will be end, starting from the first byte of header
    Transaction ID (xid)
      A unique value used to match requests to response
Bit Offset | 0 ~ 7 | 8 ~ 15 | 16 ~ 23 | 24 ~ 31
0 ~ 31 | Version | Type | Message Length | 
32 ~ 63 | Transaction ID |  |  | 
64 ~ ? | Payload |  |  | 
OpenFlow Message Structure

## Slide 16: OpenFlow Protocol Messages
Category | Message | Type | Description
Meta Info. Configuration | Hello (SM) | C  S | following a TCP handshake, the controller sends its version number to the switch.
 | Hello (SM) | S  C | the switch replies with its supported version number.
 | Features Request (CSM) | C  S | the controller asks to see which ports are available.
 | Set Config (CSM) | C  S | in this case, the controller asks the switch to send flow expirations.
 | Features Reply (CSM) | S  C | the switch replies with a list of ports, port speeds, and supported tables and actions.
 | Port Status | S  C | enables the switch to inform that controller of changes to port speeds or connectivity..
Flow Processing | Packet-In (AM) | S  C | a packet was received and it didn't match any entry in the switch's flow table, causing the packet to be sent to the controller.
 | Packet-Out (CSM) | C  S | Instructs a switch to send a packet out to one or more switch ports.
 | Flow-Mod (CSM) | C  S | instructs a switch to add a particular flow to its flow table.
 | Flow-Expired (CSM) | S  C | a flow timed out after a period of inactivity.
C: OpenFlow Controller
S: OpenFlow Switch
AM: Asynchronous message CSM: Control/Switch Message SM: Symmetric Message

## Slide 17: OpenFlow Communication
Connection Setup

## Slide 18: OpenFlow: Flow Table
Flow Table
Counters used when controller calculates paths
Actions(Instructions)
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Modify Fields
Etc.
Switch
Port
MAC src
MAC
dst
Ether type
VLAN ID
VLAN Priority
MPLS Label
MPLS traffic class
Src
IP
Dst
IP
Protocol No.
ToS
Src
TCP/UDP port
Dst
TCP/UDP port
Meta data
L2
L1
L3
L4
Flow entry
match field
counter
Action
(Instruction)
n
…
…
…
1
priority
Timeout
Flow table
Match fields of OpenFlow 1.1
cookie
Match field= L1~L4 header information
  OpenFlow 1.0  12 tuples
  OpenFlow 1.1  15 tuples
  OpenFlow 1.3  40 tuples (158 bytes)

## Slide 19: OpenFlow: Flow Table
Flow Table
  Wild card (*) means “does not matter” – not important field

## Slide 20: OpenFlow Pipelining
Pipelining
  The flow tables of a switch are sequentially numbered, starting at 0
  A packet is processed sequentially in multiple flow tables (version 1.1)
    If a flow entry is found, the instruction set included in that flow entry is executed
    Instructions may explicitly direct the packet to another flow table (“goto-table”)
    Pipeline processing can only go forward and not backward
  Two stage pipeline processing (version 1.5)
    Ingress processing
      Mandatory, performed before egress processing, use the rules specified in ingress tables
    Egress processing
      Optional, performed in the context of output port, use the rules specified in egress tables
      Egress table can be configured during feature request/reply phase
  Useful to manage complicated processing
    E.g., table 1 for VLAN processing, table 2 for multicast group processing
Flow Table 0
Instruction/Action
Flow Table n
Instruction/Action
Ingress processing
…
Packet In
Group Table
Flow Table e
Instruction/Action
Flow Table e+m
Instruction/Action
Egress processing
…
Packet Out

## Slide 21: Packet Processing Flowchart in OF Switch
Packet In
Packet Out
Match in table n?
Table-miss flow entry exists?
Goto-Table n?
Group action?
Output action?
Switch has egress tables?
Drop packet
Drop packet
Update counters
Execute instruction set:
Update action set
Update packet headers
Update match set fields
Update pipeline fields
As needed, clone packet to egress
Execute action set:
Update packet headers
Update match set fields
Update pipeline fields
Yes
Yes
Yes
Yes
Yes
Yes
No
No
No
No
No
Ingress
Egress
Start egress processing:
Action set = {output port}
Start at first egress table
Match in table n?
Table-miss flow entry exists?
Goto-Table n?
Output action?
Drop packet
Update counters
Execute instruction set:
Update action set
Update packet headers
Update match set fields
Update pipeline fields
As needed, clone packet to egress
Execute action set:
Update packet headers
Update match set fields
Update pipeline fields
No
Yes
Yes
Yes
No
No
No
Drop packet
Yes
No

## Slide 22: Instructions in OpenFlow
Instructions
  Instructions are executed when a packet matches an entry in a table
  Instructions result in changes to the packet, action set and/or pipeline processing
Syntax | Description
Meter meter_id | Direct packet to the specified meter
Apply-Actions actions | Apply the specific actions immediately. Execute multiple actions of the same type.
Clear-Actions | Clear all the actions in the action set immediately
Write-Actions actions | Merge the specified actions into the current action set, if exists try to overwrite, otherwise try to add.
Goto-Table next-table-id | Indicate the next table in the processing pipeline. The table-id must be greater than the current table-id.

## Slide 23: Actions in OpenFlow
Actions
  An action is associated with each packet
  When the instruction set does not contain a Goto-Table instruction, pipeline processing stops and the actions are executed
Syntax | Description
set | Apply all set-field actions to the packet
qos | Apply all QoS actions, such as set_queue to the packet
group | If a group action specified, apply the actions of the relevant group bucket(s) in the order specified by this list
output | If no group action is specified, forward the packet on the port specified by the output action
push_MPLS | Apply MPLS tag push action to the packet
push_VLAN | Apply VLAN tag push action to the packet
pop | Apply all tag pop actions to the packet

## Slide 24: OpenFlow Group Table
Group Table & Types (version 1.1)
  All: multicast
  Select: load sharing
  Indirect: simple indirection
  Fast-failover: rerouting
Table 0
Instruction/Action
Table 1
Instruction/Action
Table n
Instruction/Action
……
Action
Bucket
Group Table
Match field
Counter
Action
Group ID
Counter
Action buckets
Group type
Dst IP= 224.2.3.9
Flow table
Group table
Group 100
100
all
Port1 : output
Port3 : output
Port5 : output
………
Multicast
Load sharing
Indirection
Rerouting

## Slide 25: OpenFlow Group Table
Multicast
  Type=all
Group ID | Group Type | Counter | Action Buckets
100 | All | 999 | Port2, Port3, Port4
Group Table
Switch Port | MAC src | MAC dst | Ether Type | VLAN ID | Src IP | Dst IP | Proto No. | TCP S Port | TCP D Port | Action
* | * | 00:FF:.. | * | * | * | * | * | * | * | Port 6
Port 1 | * | * | 0800 | * | 224… | 224… | 4 | 4566 | 6633 | Group 100
Flow Table
2
3
4
1

## Slide 26: OpenFlow Group Table
Load Balancing
  Type=select
Group ID | Group Type | Counter | Action Buckets
100 | Select | 999 | Port2, Port3
Group Table
Switch Port | MAC src | MAC dst | Ether Type | VLAN ID | Src IP | Dst IP | Proto No. | TCP S Port | TCP D Port | Action
* | * | 00:FF:.. | * | * | * | * | * | * | * | Port 1
Port 1 | * | * | 0800 | * | 1.2.3… | * | 4 | * | 80 | Group 100
Flow Table
2
3
1

## Slide 27: OpenFlow Group Table
Indirection
  Type=indirect
Group ID | Group Type | Counter | Action Buckets
100 | Indirect | 777 | Port 5
Group Table
Switch Port | MAC src | MAC dst | Ether Type | VLAN ID | Src IP | Dst IP | Proto No. | TCP S Port | TCP D Port | Action
* | 00:FF… | * | 0800 | * | 1.2.2… | 11.1… | * | * | * | Group 100
* | 00:FF... | * | 0800 | * | 1.2.3… | 11.1… | * | * | * | Group 100
Flow Table
2
3
4
1
5

## Slide 28: OpenFlow Group Table
Fast Failover
  Type=fast-failover (ff)
Group ID | Group Type | Counter | Action Buckets
100 | Fast-failover | 777 | Port4, Port5, Port6
Group Table
Switch Port | MAC src | MAC dst | Ether Type | VLAN ID | Src IP | Dst IP | Proto No. | TCP S Port | TCP D Port | Action
Port 1 | * | * | * | * | 1.2.2 | * | * | * | * | Port 7
Port 1 | 00:FF… | * | 0800 | * | 1.2.3… | 11.1… | * | * | * | Group 100
Flow Table
2
3
4
1
5
6

## Slide 29: OpenFlow Meter Table
Meter Table (ver 1.3)
  Counts packet rate of a matched flow
  QoS control  Rate-limit, DiffServ …
Meter ID | Band Type | Rate | Counter | Argument
100 | Drop (remark DSCP) | 1000 kbps | 1000 | xxx
Meter Table
Switch Port | MAC src | MAC dst | Ether Type | Src IP | Dst IP | Proto No. | TCP S Port | TCP D Port | Inst. Meter | Action
Port 1 | * | * | * | 1.2.2 | * | * | * | * | N/A | Port 7
Port 1 | 00:FF… | * | 0800 | 1.2.3… | 11.1… | * | * | * | Meter 100 | Port 2
Flow Table

## Slide 30: Packet Forwarding in OpenFlow
Packet Forwarding
  Reactive flow insertion
    A non-matched packet reaches to OpenFlow switch, it is sent to the controller, based on the info in packet header, an appropriate flow will be inserted
    Always need to query the path from controller during packet arrival  slow
    Can reflect the current traffic status
  Proactive flow insertion
    Flow can be inserted proactively by the controller to switches before packet arrives
    No need to communicate during packet arrival  fast packet forwarding
    Cannot reflect the current traffic status
OpenFlow Controller
host1
host2
switch1 (reactive)
switch2 (proactive)
acquire route
insert flow
SRC | DST | ACT | …
SRC | DST | ACT | …
h1 | h2 | p2 | 
2
1
2
1
h1 h2 p2

## Slide 31: Topology Discovery in OpenFlow
Purpose
  To construct an entire network view
Method
  Use the Link Layer Discovery Protocol (LLDP)
LLDP
PACKET_OUT with LLDP
PACKET_OUT with LLDP
PACKET_IN with LLDP
OpenFlow Controller
IDX | SRC | DST | SRC PORT | DST PORT
153 | sw. A | sw. B | p2 | p1
… | … | … | … | …
357 | sw. B | sw. A | P1 | p2
p1
p2
p1
p2
Notes: OpenFlow Switch 포트의 status 정보를 스위치에서 Controller에 보내면서 Topology Discovery가 이루어진다.
스위치의 포트가 Down에서 Up으로 변경된다.
이 포트의 변경 사항을 Switch에서 Controller에 보낸다.
Controller는 LLDP가 Switch의 변경된 포트를 통해 전송되도록 Packet Out Message로 생성하여 전송한다.
이것을 수신한 Switch는 Packet Out Message에 담긴 LLDP를 인접한 Switch에 전달한다.
LLDP를 받은 인접한 Switch는 해당 LLDP를 어떻게 처리해야 할지를 모르기 때문에 이 Packet을 Controller에 Packet In Message 형태로 보낸다.
Controller는 이를 통해 스위치 간 연결 정보를 확인한다.

## Slide 32: Communication in Legacy Network
host2
host1
switch1
switch2
$ ping 10.1.1.11
IP: 10.1.1.12
MAC:00:50:56:86:16:C8
IP: 10.1.1.11
MAC:00:50:56:86:0A:AE
ping
switch3
switch4
host3
IP: 10.1.1.13
MAC:00:50:56:86:16:99
host4
IP: 10.1.1.14
MAC:00:50:56:86:18:78
Internet Address Physical Address Type
10.1.1.254 00-00-0C-E7-58-CD Dynamic
  host2 creates entry to ARP Cache Table
  host2 sends ICMP Echo request packet
  host1 replies ICMP Echo request with ICMP Echo reply
ARP Cache Table of Host2
  host2 tries communication to host1 by sending a ping ICMP packet
  host2 broadcasts ARP Request packet
  host1 replies ARP Request with ARP Reply
10.1.1.11 00-50-56-86-0A-AE Dynamic
ARP Request
ARP Reply
ICMP Echo Request
ICMP Echo Reply

## Slide 33: Communication in OpenFlow
host2
host1
switch1
switch2
$ ping 10.1.1.11
IP: 10.1.1.12
MAC:00:50:56:86:16:C8
IP: 10.1.1.11
MAC:00:50:56:86:0A:AE
ping
switch3
switch4
host3
IP: 10.1.1.13
MAC:00:50:56:86:16:99
host4
IP: 10.1.1.14
MAC:00:50:56:86:18:78
Internet Address Physical Address Type
10.1.1.254 00-00-0C-E7-58-CD Dynamic
ARP Cache Table of Host2
ARP Request
Packet In
If controller has no host1 information
Packet Out
Packet In/Out
Packet In/Out
Packet In/Out

## Slide 34: Communication in OpenFlow
host2
host1
switch1
switch2
$ ping 10.1.1.11
IP: 10.1.1.12
MAC:00:50:56:86:16:C8
IP: 10.1.1.11
MAC:00:50:56:86:0A:AE
switch3
switch4
host3
IP: 10.1.1.13
MAC:00:50:56:86:16:99
host4
IP: 10.1.1.14
MAC:00:50:56:86:18:78
Internet Address Physical Address Type
10.1.1.254 00-00-0C-E7-58-CD Dynamic
ARP Cache Table of Host2
10.1.1.11 00-50-56-86-0A-AE Dynamic
ARP Reply
If controller has no host1 information
Packet In
Packet Out
Flow Mod
Packet In
Packet Out
Flow Mod

## Slide 35: Communication in OpenFlow
host2
host1
switch1
switch2
$ ping 10.1.1.11
IP: 10.1.1.12
MAC:00:50:56:86:16:C8
IP: 10.1.1.11
MAC:00:50:56:86:0A:AE
switch3
switch4
host3
IP: 10.1.1.13
MAC:00:50:56:86:16:99
host4
IP: 10.1.1.14
MAC:00:50:56:86:18:78
Internet Address Physical Address Type
10.1.1.254 00-00-0C-E7-58-CD Dynamic
ARP Cache Table of Host2
ICMP Echo Request
Packet In
Controller now has the host1 info.
Packet Out
Packet In
Flow Mod
Packet Out
Flow Mod
10.1.1.11 00-50-56-86-0A-AE Dynamic

## Slide 36: Communication in OpenFlow
host2
host1
switch1
switch2
$ ping 10.1.1.11
IP: 10.1.1.12
MAC:00:50:56:86:16:C8
IP: 10.1.1.11
MAC:00:50:56:86:0A:AE
switch3
switch4
host3
IP: 10.1.1.13
MAC:00:50:56:86:16:99
host4
IP: 10.1.1.14
MAC:00:50:56:86:18:78
Internet Address Physical Address Type
10.1.1.254 00-00-0C-E7-58-CD Dynamic
ARP Cache Table of Host2
10.1.1.11 00-50-56-86-0A-AE Dynamic
ICMP Echo Reply
Controller now has the host1 info.
Packet In
Packet Out
Flow Mod
Packet In
Packet Out
Flow Mod

## Slide 37: OpenFlow Failover
OpenFlow Failover
  Protection
Controller
A
B
C
D
E
Host 1
Host 2
Working path
Backup path
Set working and backup paths
1. Switch A detects port down
2. Send packets to the backup path
Working and backup paths are pre-inserted into all switches in advance
src | dst | Out port | Failover port
h1 | h2 | 2 | 3
Flow table of Switch A (group table combined)
1
2
3

## Slide 38: OpenFlow Failover
OpenFlow Failover
  Restoration
Controller
A
B
C
D
E
Host 1
Host 2
Port down message
Port down message
1. Obtain affected flows (host1host2)
2. Find an alternative path for each flow
path: <ACED>
3. Set up alternative paths
Working path
Backup path

## Slide 39: OpenFlow Example
Example of Routing Control (hop-by-hop routing)
Virtual switch C
Virtual switch D
Virtual switch A
Virtual switch B
Web Server 1 (VM3)
Web Server 2 (VM4)
AAA
(VM1)
Firewall(VM2)
PC_A
PC_B
OFSW_1
OFSW_2
OFSW_3
OFSW_4
MAC=b
MAC=a
1
2
3
4
5
6
MAC=c
MAC=d
Flow table of OFSW_1
Match Fields |  |  |  | Actions
Phy port | Src MAC | Dst MAC | VLAN ID | 
1 | a | d | 1 | Forward to p3
3 | a | d | 1 | Forward to p2
2 | a | d | 1 | Forward to p5

## Slide 40: Related Work: NFV (Network Function Virtualization)
2012 Sep., Telcos Proposed NFV
  AT&T, Verizon, BT, DT, NTT, Telefonica, China Mobile…
  NFV committee (ISG: Industry Specification Group) was setup under ETSI
  Current SDN/OpenFlow is Data Center oriented…
  Proposed to develop new virtualization technologies which allows to abstract underlying hardware… development of API for NFV
    Hopes to replace a large variety of vendor-proprietary nodes and hardware appliances
    Can reduce CAPEX, OPEX (including space & power consumption)
NMSs
OSSs
Center Router
GSR
GES
Metro SW
L3
L2
Server Farm
AAA
Mail
DNS
Core Router
DDNS
F/W
Cache
IGP
IMS
NAT
DHCP
VLAN
ACL
STB
G/W
BSSs
EMSs
DPI
DPI

## Slide 41: NFV (Network Function Virtualization)
NFV Definition
  NFV is a network architecture concept
  Virtualize the entire classes of network node functions into building block that may be connected, or chained, to create comm. Services
Relationship to SDN
Notes: In essence, Software-defined networking (SDN) is an approach to building data networking equipment and software that separates and abstracts elements of these systems. It does this by decoupling the control plane and data plane from each other, such that the control plane resides centrally and the forwarding components remain distributed. The control plane interacts both northbound and southbound. In the northbound direction the control plane provides a common abstracted view of the network to higher-level applications and programs using APIs. In the southbound direction the control plane programs the forwarding behavior, using device level APIs, of the physical network equipment distributed around the network.
Thus, NFV is not dependent on SDN or SDN concepts. It is entirely possible to implement a virtualized network function (VNF) as a standalone entity using existing networking and orchestration paradigms. However, there are inherent benefits in leveraging SDN concepts to implement and manage an NFV infrastructure, particularly when looking at the management and orchestration of VNFs, and that's why multivendor platforms are being defined that incorporate SDN and NFV in concerted ecosystems.[12]
An NFV infrastructure is more than simply adapting existing network applications to run on x86 technology. It needs a central orchestration and management system that takes operator requests associated with a VNF, translates them into the appropriate compute, storage and network configuration needed to bring the VNF into operation. Once in operation, the VNF potentially needs to be monitored for capacity and utilization and adapted if necessary.
All these functions can be accomplished using SDN concepts and NFV could be considered one of the primary SDN use cases in service provider environments. It is also apparent that many SDN use-cases could incorporate concepts introduced in the NFV initiative. Examples include where the centralized controller is controlling a distributed forwarding function that could in fact be also visualized on existing compute or routing equipment.

## Slide 42: NFV (Network Function Virtualization)
Benefits of NFV
  Standard APIs  third party S/W vendors will speed up the dev.
  More effective resource utilization
    Virtualization allows Telco to allocate necessary resources
  Easy to manage, reduce CAPEX/OPEX
Example of NFV
  NEC + Telefonica
  Impl. of EPC (Evolved Packet Core)  first demo at MWC 2013
  General purpose computers (CAPEX, OPEX  50%)
    Flexibly respond to the change of traffic with cloud computing technologies
    Innovative technology to lower Entry barrier of Telco business
MME
S/P-GW

## Slide 43: Example: Kanazawa General Hospital (with NEC solution)
Problem
  Individual network optimization led to complex network structure
    Configuration errors
    Rewiring whenever a new equipment is connected
    Difficult to find fault location
Lobby, registration
Emergency Room
Surgery
Servers
F/W x 2
F/W x2
L3 Core Switch

## Slide 44: Example: Kanazawa General Hospital (with NEC solution)
Solution
  16 OpenFlow switches and 2 controllers
  Create virtual network/department
  Flow patch control
    Save CAPEX and OPEX
  Fast recovery from failure
OpenFlow Controller x2
OpenFlow Switch x2 /floor x 7 floor
L3 Core switch
Full nesh N/W
F/W pool
Server pool
Notes: MTTR: Mean time to repair
A basic measure of the maintainability of repairable items. It represents the average time required to repair a failed component or device.

## Slide 45: Q&A