## Slide 1
Network Softwarization: SDN/NFV and Open Networking
Prof. James Won-Ki Hong
Distributed Processing and Network Management (DPNM) Lab.
Dept. of Computer Science & Engineering
POSTECH
Pohang, South Korea
http://dpnm.postech.ac.kr/
jwkhong@postech.ac.kr
2023. 2. 14

## Slide 2
Outline
Evolution of Networks
Challenges for Telecom operators
SDN
NFV
Open Networking Ecosystem
SDN/NFV Use Cases
SDN/NFV Forums, Conferences & Journals
Concluding Remarks
Glossary & References

## Slide 3
Short Bio
Education
  1991 – PhD in Computer Science, Univ. of Waterloo, Canada
  1985 – MSc in Computer Science, Univ. of Western Ontario, Canada
  1983 – HBSc in Computer Science, Univ. of Western Ontario, Canada
Professional Activities
  Co-Founder & Technical Advisor, Kedutech, Korea (2020. 8 – present)
  Director, POSTECH Innovation Center for Education (Nov. 2019 – present)
  Executive Director, SDN/NFV Forum (2014.10 – 2019. 4)
  CTO & SEVP, KT (Korea Telecom) (2012. 3 – 2014. 2)
  President, Intelligent Communication Industry Association (2013.1 - 2014.2)
  Chairman, Korea ICT Standards Committee (2012.3 – 2014.2)
  Dean, Graduate School of Information Technology, POSTECH (2007.3 – 2012.2, 2015.11 – 2019.10)
  Head, Division of IT Convergence Engineering, POSTECH (2008.12 – 2012.2)
  Head, Dept. of Computer Science and Engineering, POSTECH (2008.12 – 2010.02)
  Director, POSTECH Information Research Labs (2007.9 – 2010.02)
  Professor, Dept. of Computer Science and Engineering, POSTECH (1995.5 – present)
  Research Professor, Univ. of Western Ontario, Canada (1992.5 – 1995.4)
  Editor-in-Chief, Int. Journal of Network Management (2012.1-present)
  Editorial Board Member of IEEE TNSM, JCN, JNSM
  IEEE Communications Society Member-at-Large (2015.1 – 2017.12)
  Co-Founder & CTO, Netstech, Palo Alto, USA (2000.6 – 2002.2)
  Steering Committee Member of IEEE NOMS, IM, APNOMS, CNSM, NetSoft, NFV-SDN
  General Chair (IEEE ICBC 2019, NOMS 2018, NetSoft 2016, NOMS 2010, APNOMS 2008 & 2006)
  Technical Chair (2001-2002) & Chair (2005-2009), IEEE ComSoc CNOM
Prof. James Won-Ki Hong
30+ Years Education Experience in Canada & Korea
Global Startup Experience
Industry Senior Executive Experience
Notes: I will present challenges that are faced by telecom operators. I will then address the recent SDN/NFV technology trend. After that, I will introduce what artificial intelligence (AI) is and how AI technology is being applied in network management. Specifically, I will introduce AI-based NFV Life Cycle management technology, which has been studied in the DPNM laboratory for the last four years. Finally, I will introduce AI-based traffic engineering and summarize this talk.

## Slide 4
Evolution of Networks

## Slide 5
Internet History
54 years later
1969
Notes: The network has been growing larger and more complex over the past five decades while adopting new technologies and services. In South Korea, Telco networks consist of hundreds of backbone routers, thousands of edge routers, and hundreds of thousands of access switches. As shown in this slide, Telco networks are built as either best-effort networks to provide general web services (e.g., email, web surfing) or premium networks to support high-quality services. In particular, premium networks are used to provide enterprise services, such as VPNs and IPTVs, requiring high reliability and high quality, and mobile services, such as 4G and 5G.
Thousands of middleboxes are being virtualized based on cloud computing and NFV technologies to support and perform various networks functions, such as BSS/OSS/NMS/EMS, carrier-grade NAT/DNS, and firewall/DPI/IDS, in networks.

## Slide 6
Evolution of Mobile Networks
Source: https://www.researchgate.net/publication/350889195_5G_and_Beyond_Past_Present_and_Future_of_the_Mobile_Communications_English_Version
Notes: Mobile networks have been evolving over the past 5 decades, starting from 1G to 5G and soon to 6G. The new technology has been introduced every 10 years.

## Slide 7
Evolution of Mobile Communications
Source: European Commission
Notes: The network has been growing larger and more complex over the past five decades while adopting new technologies and services. In South Korea, Telco networks consist of hundreds of backbone routers, thousands of edge routers, and hundreds of thousands of access switches. As shown in this slide, Telco networks are built as either best-effort networks to provide general web services (e.g., email, web surfing) or premium networks to support high-quality services. In particular, premium networks are used to provide enterprise services, such as VPNs and IPTVs, requiring high reliability and high quality, and mobile services, such as 4G and 5G.
Thousands of middleboxes are being virtualized based on cloud computing and NFV technologies to support and perform various networks functions, such as BSS/OSS/NMS/EMS, carrier-grade NAT/DNS, and firewall/DPI/IDS, in networks.

## Slide 8
Evolution of Wireless Networks (WiFi)
Source: L-com
Notes: The network has been growing larger and more complex over the past two decades while adopting new technologies and services. In South Korea, Telco networks consist of hundreds of backbone routers, thousands of edge routers, and hundreds of thousands of access switches. As shown in this slide, Telco networks are built as either best-effort networks to provide general web services (e.g., email, web surfing) or premium networks to support high-quality services. In particular, premium networks are used to provide enterprise services, such as VPNs and IPTVs, requiring high reliability and high quality, and mobile services, such as 4G and 5G.
Thousands of middleboxes are being virtualized based on cloud computing and NFV technologies to support and perform various networks functions, such as BSS/OSS/NMS/EMS, carrier-grade NAT/DNS, and firewall/DPI/IDS, in networks.

## Slide 9
Evolution of Optical Networks
Source: Huawei
Notes: The network has been growing larger and more complex over the past two decades while adopting new technologies and services. In South Korea, Telco networks consist of hundreds of backbone routers, thousands of edge routers, and hundreds of thousands of access switches. As shown in this slide, Telco networks are built as either best-effort networks to provide general web services (e.g., email, web surfing) or premium networks to support high-quality services. In particular, premium networks are used to provide enterprise services, such as VPNs and IPTVs, requiring high reliability and high quality, and mobile services, such as 4G and 5G.
Thousands of middleboxes are being virtualized based on cloud computing and NFV technologies to support and perform various networks functions, such as BSS/OSS/NMS/EMS, carrier-grade NAT/DNS, and firewall/DPI/IDS, in networks.

## Slide 10
Evolution of Data Centers
Notes: The network has been growing larger and more complex over the past two decades while adopting new technologies and services. In South Korea, Telco networks consist of hundreds of backbone routers, thousands of edge routers, and hundreds of thousands of access switches. As shown in this slide, Telco networks are built as either best-effort networks to provide general web services (e.g., email, web surfing) or premium networks to support high-quality services. In particular, premium networks are used to provide enterprise services, such as VPNs and IPTVs, requiring high reliability and high quality, and mobile services, such as 4G and 5G.
Thousands of middleboxes are being virtualized based on cloud computing and NFV technologies to support and perform various networks functions, such as BSS/OSS/NMS/EMS, carrier-grade NAT/DNS, and firewall/DPI/IDS, in networks.

## Slide 11
Challenges for Telecom operators (Telcos)

## Slide 12
Challenges for Telcos
Center
Router
Core Router
Core
Router
GSR
Server Farm
GSR
Core
Router
Core
Router
Global Hub
Foreign Carriers
1
1
Data Centers
IX
Other Carriers
Telco Networks
NAT
IDS
IPS
DPI
BSS
OSS
NMS
EMS
Web
FW
S-GW
P-GW
PCRF
HSS
MME
SGSN
eNodeB
EPC Core
best-effort
premium
Notes: The network has been growing larger and more complex over the past two decades while adopting new technologies and services. In South Korea, Telco networks consist of hundreds of backbone routers, thousands of edge routers, and hundreds of thousands of access switches. As shown in this slide, Telco networks are built as either best-effort networks to provide general web services (e.g., email, web surfing) or premium networks to support high-quality services. In particular, premium networks are used to provide enterprise services, such as VPNs and IPTVs, requiring high reliability and high quality, and mobile services, such as 4G and 5G.
Thousands of middleboxes are being virtualized based on cloud computing and NFV technologies to support and perform various networks functions, such as BSS/OSS/NMS/EMS, carrier-grade NAT/DNS, and firewall/DPI/IDS, in networks.

## Slide 13
Challenges for Telcos
A rapid increase in data volume in Telco Networks
 | More Mobile Users | More Traffic Volume (per month) | More Mobile Video | Faster Mobile Speeds
2015 | 4.8 Billion | 3.7 EB | 55% of Traffic | 2.0 Mbps
2018 | 5.1 Billion | 30.6 EB | 75% of Traffic | 6.5 Mbps
2023 | 5.7 Billion | 224.08 EB | 80% of Traffic | 43.9 Mbps
Source: CISCO VNI Global Mobile Data Traffic Forecast, 2015-2020 & 2018-2023
CAPEX, OPEX
Increase!!!
Notes: In Telco networks, traffic volume began to grow around 2007 drastically, when smartphones began to spread worldwide. The data traffic is still growing more than 20% per year. In the case of mobile communication, data traffic was audio traffic in the 2G era. However, with the advent of smartphones and mobile communication services through 3G, 4G, and 5G, most of the data traffic has been audio, video streaming, and web browsing. Although Telcos continue to increase network capacity to cope with this increase in traffic, reduction of CAPEX/OPEX is a challenge for Telcos as global subscriber growth continues to decline.

## Slide 14
Challenges for Telcos
Reduced revenue share in Telco’s Business Model
  Changes in Business model
    Closed Market (Feature phone era)
    Open Market (Smartphone era)
      Telco’s Share? 0%
  TTM (Time to Market)
70%
30%
Content Providers (App Developers)
App. Stores
(Apple, Google)
70%
30%
Content Providers
Telco
<Revenue Share>
Notes: In the 2G era, there was a competition between Telcos to attract subscribers, and there were no other competitors. Thus, Telcos were able to earn stable revenue. However, the smartphone era changed the situation a lot. New content and service providers, i.e., Internet players, such as Google, Amazon, and Facebook, have emerged as powerful competitors for Telcos. They were much more innovative in their operations and faster time-to-market than Telcos.
It might be due to manpower efficiency differences between service providers and Telcos. However, the main reason was that Telcos used a hardware-based communication system that was less flexible, so it took much longer to develop and provide new services. After all, Telcos invested a lot of money to build high-speed wired and wireless networks, but they could not earn more revenue. Instead, Internet players, such as Google, Amazon, Facebook, and Netflix made high revenue by using the networks.

## Slide 15
Challenges for Telcos
Infrastructure of Internet players (e.g., Amazon, MS, Google)
  Rents cloud computing & storage resources to operate services
  Builds a data center using bare metal servers & switches running open source software
     Inexpensive, flexible, dynamic
Infrastructure of Telecom operators
  Tens of thousands of blackboxes (Router, Switch, Middlebox)
  Cable, tower, antenna
   Very expensive, inflexible, static
  It is desirable to change the infrastructure of Telcos!
Notes: Internet players, such as Amazon, Microsoft, and Google do not build networks themselves. Instead, they build data centers or rent cloud computing and storage resources to provide services. When building a data center, they design hardware and make vendors compete to implement it at a low cost. After that, Internet players select a vendor that provides the cheapest hardware. In addition, open-source software, such as Linux and Apache, is used to build a dynamic and flexible infrastructure at a low cost. Thus, Internet players can deploy their infrastructure dynamically and flexibly at a low cost.
(Click) On the other hand, Telcos have built networks composed of expensive hardware-based entities and have operated services on the infrastructure. In addition, it was hard for telcos to adopt new technologies quickly due to vendor dependency and incompatibility issues of network entities. As a result, Telcos are aware of the need to change their networks and service environments into a similar and competitive infrastructure of Internet players.

## Slide 16
Challenges for Telcos
Mobile Instant Messaging Apps (as of Mar. 2022)
KakaoTalk (Korea)
WhatsApp (USA)
Started: Nov. 2009
Monthly Active Users: 2.0 Billion
Dominant: USA, Europe, Brazil, Mexico, India
Acquired by Facebook (Feb. 2014)
for $19B
Started: March 2010
Monthly Active Users: 50 Million
Dominant: Korea (90% of Koreans use)
Revenue from gaming, emoticon, finance
90% drop in Telco SMS Usage for last 10 years in Korea
Line (Japan/Taiwan/Thailand)
WeChat (China)
Started: Jan. 2011
Monthly Active Users: 1.26 Billion
Dominant: China but growing in USA, Europe & Africa
Revenue from gaming, shopping, banking
Started: June 2011
Monthly Active Users: 187 Million
Dominant: Japan, Taiwan, Southeast Asia and South America
Revenue from gaming, stickers, ads
Source: techcrunch.com, Statista (www.statista.com), DMR (https://expandedramblings.com)
Why are these apps challenge to Telcos?

## Slide 17
Challenges for Telcos
In the current era, where costs are rising but revenues and profits are continuously falling, how can Telcos reduce CAPEX & OPEX and have a flexible, agile and efficient operations environment to have a chance to compete against Internet players (such as Google, Apple, Amazon, Facebook, Microsoft, Naver, Kakao, Tencent, Baidu, Alibaba, etc.)?
 SDN/NFV = ‘Network Softwarization’ is a promising & desperately needed approach for telco service infrastructures

## Slide 18
Challenges for Telcos
Comparison to the Compute Paradigm
  Compute paradigm for the past few decades
  Benefits
    Open/flexible choices and cost-effective solutions for customers
    Rapid innovation (CPU, OS, Applications)
    Rich ecosystem

## Slide 19
Challenges for Telcos
Comparison to the Compute Paradigm
  SDN/NFV is changing the paradigm in networking area

## Slide 20
SDN/NFV
(Open Networking)

## Slide 21
SDN/NFV
Legacy Network
SDN/NFV – Key to network evolution
Center Router
Core Router
GSR
GES
Metro SW
L3
L2
Server Farm
AAA
Mail
DNS
DDNS
Firewall
Cache
Cache
IGMP
NAT
DHCP
VLAN
ACL
BSS
OSS
NMS
NMS
NMS
NMS
EMS
STB
DPI

## Slide 22
SDN
Software Defined Networking (SDN)
  Separates the control plane from the underlying data plane
  Supports the centralized management (SDN controller)
Features of SDN
  Programmability
  Agility
  Flexibility
  Vendor neutrality
  CAPEX/OPEX saving
Control Plane
Data Plane
Mgmt.
Plane
Traditional Network
SDN
Controller
OpenFlow
Flow Table
Notes: As you may already know, SDN is a technology that separates the control plane from the underlying data plane of the communication system. It allows the control plane that is complex and hard for implementing to be operated in a centralized manner based on cloud computing. Thus, it is possible to build networks without expensive network entities. In addition, SDN supports network programmability and provides vendor neutrality by building software-based infrastructures.

## Slide 23
NFV
Network Function Virtualization (NFV)
  Replaces physical hardware with software
  Uses the technologies of IT virtualization to virtualize network functions to reduce costs and improves flexibility, operability, and maintenance
Source: https://www.tekedia.com/5-0-5g-core-5gc/
Notes: Network Function Virtualization, NFV, is a technology that significantly reduces CAPEX and provides easy-to-use network functions by leveraging open-source software from white boxes instead of using expensive middleboxes described in the previous slide.

## Slide 24
SDN/NFV
Source: https://eogogics.com/enhancing-network-capacity-functionality-sdn-nfv/, https://blog.advaoptical.com/en/nfv-and-sdn-the-roadmap-to-programmable-networks
Virtualized Network Function (VNF)
SDN can support flexible chaining of VNFs (in servers, data centers)
to provide agile and efficient network services
Notes: With a combination of SDN and NFV, middleboxes can be implemented and managed as Virtual Network Functions (VNFs). SDN can make connections between VNFs flexibly for Service Function Chaining, SFC, and apply auto scaling that adjusts resources allocated to VNFs, in response to traffic changes. Thus, SDN/NFV has the advantage of enabling powerful and flexible network operations.

## Slide 25
SDN/NFV
Source: SDx Central, 2016
Source: SDx Central, 2016
Major NFV Drivers
SDN/NFV Market
Revenue Forecast

## Slide 26
SDN/NFV
Benefits of SDN/NFV
  Operators manage VNFs in a centralized manner and configure networks optimally while considering network status
  It reduces telco operator’s dependency on vendor-specific hardware
  It manages VNFs rapidly in response to network environment changes
Limitations
  Increased complexity in network management
    Network management is getting difficult due to a massive amount of network traffic
    Additional SDN/NFV entities complicate network management
  Increase in vulnerability
    SDN/NFV enables network operators to configure network environment rapidly and flexibly, but it can cause network failure frequently due to the wrong configuration
A new approach for network management is required  Application of AI technology
Notes: The introduction of SDN and NFV has dramatically reduced costs while enabling flexible and dynamic infrastructure operations.
(Click) However, the network scale and complexity have also increased significantly due to SDN/NFV. Specifically, Virtual Machines (VMs) run VNFs, so there are numerous VMs in networks, making it human operators hard to handle them manually. In addition, the transformation from hardware-based to open-source software-based environment causes vulnerability issues generating network failures frequently. As a result, it is too difficult to manage the complex network by human operators. Thus, R&D approaches using artificial intelligence (AI) have been proposed to solve the complicated network management in the past few years.

## Slide 27
Open Networking Ecosystem

## Slide 28
Open Networking Ecosystem
Open Networking Reference Model
Source: Huawei
Hardware
Programmable Data Plane Services
Network Controllers
Carrier Networking Functions
Compute Server Operating Systems
Containers
VM/VI Managers
Application Platforms
Programming Frameworks
Network Switch Operating Systems
Management & Orchestration
Virtual Machines

## Slide 29
Software-Defined Networking
(SDN)

## Slide 30
Open Networking Ecosystem
Hardware
  P4 (programming protocol-independent packet processors)
    Declarative language for telling forwarding-plane devices
    (switches, NICs, firewalls, filters, etc) how to process packets
    Characteristics
      Protocol Independence
      Target Independence
      Field Re-configurability
    Members
    Contributors
      https://p4.org/join/
      https://opennetworking.org/member-listing/ (including POSTECH)

## Slide 31
Open Networking Ecosystem
Hardware
  OCP (Open Compute Project)
    Started by Facebook in 2011
    Redesign hardware technology to efficiently support the growing demands on compute & network infrastructure
    Break open the black box of proprietary IT infrastructure to achieve greater choice, customization, and cost savings
    Projects
      Server Design
      Storage
      Data Center
      Hardware Management
      Networking
      Open Rack
      Certification
    https://www.opencompute.org/
Members

## Slide 32
Open Networking Ecosystem
Network Switch Operating Systems
  OpenSwitch (OPX)
    Linux based operating system originally developed by HP
      For OCP compliant hardware
    Includes full L2/L3 switching functions
      Routing / OpenFlow agents are included
    Members
    https://www.openswitch.net/

## Slide 33
Open Networking Ecosystem
Network Switch Operating Systems
  ONL (Open Network Linux)
    Linux distribution for "bare metal" switches
      A collection of software packages, utilities, drivers,
      and abstractions to run on OCP Switch hardware (https://opennetlinux.org/)
    Members
Open Network Linux | OpenSwitch
Features / Functionalities | 
- OpenPlatform Distribution for NOS - Routing / OpenFlow agents NOT included (only samples) | - Open NOS with full L2/L3 Switching functionalities - Routing/ OpenFlow agents are included
Target Hardware | 
OCP (Open Compute) Switch, Bare metal (White Box) Switch | 
Contributors | 
Big Switch Networks, Pica8, Accton | HP Enterprise, Accton, Broadcom Intel, Qosmos, VMWare, Arista
License | 
Eclipse Public License and GPL for Kernel | Apache License, v. 2.0
Source: “Open Network Linux: A Programmer’s View”, Big Switch Networks

## Slide 34
Open Networking Ecosystem
Programmable Data Plane Services
  DPDK
    A set of libraries and drivers for fast packet processing by bypassing OS kernel
    Enables faster development of high-speed data packet networking applications
    Supported processors
      Intel x86, IBM Power 8, EZchip TILE-Gx, ARM, etc. (https://core.dpdk.org/supported/)
  FD.io
    Create a platform that enables Data Plane Services that are:
      Highly performant
      Modular and extensible
      Open source, Interoperable, Multi-vendor
    Usable in cloud, VMs, containers, bare metal and others
Members

## Slide 35
Open Networking Ecosystem
Programmable Data Plane Services
  Open vSwitch (OvS)
    Open source software switch used as a virtual switch in virtualized server environments
    Leverages OpenFlow and Open vSwitch Database (OVSDB) management protocol
    Runs on any Linux-based virtualization platform
      KVM, VirtualBox, Xen
    Members
    https://www.openvswitch.org/
Source: https://en.wikipedia.org/wiki/Open_vSwitch

## Slide 36
Open Networking Ecosystem
Network Controllers
  ONOS (Open Network Operating System)
    Open source SDN network OS from ONF (formerly ON.Lab)
    The goal is to create a SDN OS for service providers (Carriers)
    Provides scalability, high availability, high performance and abstractions
    https://onosproject.org/
    Members

## Slide 37
Open Networking Ecosystem
Network Controllers
  ODL (OpenDaylight)
    A collaborative open source SDN controller project managed by Linux Foundation
    Most of the global hardware & software vendors are members
    Modular Open SDN platform for networks
    Provides a model-driven service abstraction platform
    Members

## Slide 38
Network Function Virtualization (NFV)

## Slide 39
Open Networking Ecosystem
Carrier Networking Functions
  OPNFV (Open Platform for NFV Projects)
    A carrier-grade, integrated, open source platform that accelerates the introduction of new NFV products and services
    Brings together network functions across compute, storage and network virtualization in order create an end-to-end platform
    Members
    https://www.opnfv.org/

## Slide 40
Open Networking Ecosystem
Virtual Machines
  Xen Project
    Hypervisor using a microkernel design
    Provides services that allow multiple OSes to execute on the same computer hardware concurrently
    Supports multiple guest operating systems
      Linux, Windows, NetBSD, FreeBSD
    Supports multiple Cloud platforms
      OpenStack, CloudStack
    Members
    https://xenproject.org/
Source: https://wiki.xenproject.org/wiki/Xen_Project_Software_Overview

## Slide 41
Open Networking Ecosystem
Virtual Machines
  KVM (Kernel-based Virtual Machine)
    Full virtualization solution for Linux on x86 hardware
    Merged into the Linux kernel mainline in kernel version 2.6.20
    Supports multiple guest operating systems
      Linux, BSD, Solaris, Windows, Mac OSX
    Members
    https://www.linux-kvm.org/
Source: https://computingforgeeks.com/how-to-create-vm-snapshot-on-kvm/

## Slide 42
Open Networking Ecosystem
Operating Systems
  Linux
    Best-known and most-used open source OS
    Assembled under the model of free and open-source software development and distribution
    Popular mainstream Linux distributions
      Debian, Ubuntu, Linux Mint, Fedora, openSUSE, Arch Linux and Gentoo
  FreeBSD
    OS for a variety of platforms which focuses on features, speed, and stability
    Major differences with Linux
      Complete OS vs. a kernel and drivers only
      BSD license vs. copyleft GPL

## Slide 43
Open Networking Ecosystem
Containers
  Docker
    Automates the deployment of applications inside software containers
    Provides an additional layer of abstraction and automation of OS-level virtualization on Linux
    Enables to package an application with all of its dependencies into a standardized unit for software development (https://www.docker.com/)
Source: https://www.docker.com/what-container
VMs | Containers
Entire OS installation | Multiple isolated user-space instances
Entire OS needed | Only libraries and components needed for application
VM runs using emulation or virtualization on host OS | Runs on the same kernel
Independent to host OS | Dependent to host OS (Linux)
Entire VM OS and disk images | Much smaller, easier to package
Longer to start | Faster to start
Security issues of running OS | Security limited to app
Inefficient use of resources | Efficient use of resources

## Slide 44
Open Networking Ecosystem
VMs vs. Containers
  Performance comparison
    The general result is that Docker is nearly identical to native performance and faster than KVM in every category
I/O
CPU
Network
Boot Time
Source: IBM Research Report: An Updated Performance Comparison of Virtual Machines and Linux Containers, July 21, 2014. Passive Benchmarking with docker LXC, KVM & OpenStack, IBM

## Slide 45
Open Networking Ecosystem
VM/VI Managers
  Kubernetes
    Open-source platform for automating deployment, scaling, and management of containerized applications
    Functionalities
      Auto-placement, auto-restart, auto-replication, auto-scaling
      Schedule across hosts
      Container grouping
      Load balancing
    Members
    https://kubernetes.io/
Source: https://cloudplatform.googleblog.com/2015_01_01_archive.html

## Slide 46
Open Networking Ecosystem
VM/VI Managers
  OpenStack
    Open source software platform for cloud computing
    Mostly deployed as an IaaS (like Amazon EC2)
    Controls large pools of compute, storage, and networking resources throughout a datacenter
    Core services
      swift (object storage), keystone (identity), nova (compute), neutron (networking), cinder (block storage), glance (image service)
    https://www.openstack.org/

## Slide 47
Open Networking Ecosystem
VM/VI Managers
  OpenStack Tacker
    OpenStack project building a Generic VNF Manager (VNFM) and an NFV Orchestrator (NFVO) to deploy and operate Network Services and Virtual Network Functions (VNFs)
    Based on ETSI MANO Architectural Framework

## Slide 48
Open Networking Ecosystem
Management & Orchestration
  Open Source MANO (OSM)
    Develop an Open Source NFV Management and Orchestration (MANO) software stack aligned with ETSI NFV
    Features
      End-to-end service fulfilment
      Enhanced platform awareness extensions
      SDN underlay control
      Multi-site capability
      Multi-cloud VIM capability
    Members
    https://osm.etsi.org/

## Slide 49
Open Networking Ecosystem
Management & Orchestration
  Open Network Automation Platform (ONAP)
    Brings together top global carriers and vendors to allow end users to automate, design, orchestrate and manage services/virtual functions
    Collaboration of two open networking and orchestration projects
      ECOMP and Open-O
    Members (90+, as of July 2019)
Source: http://passionateaboutoss.com/the-components-of-sdn-nfv-mano-oss/
Source: https://virtualizationreview.com/articles/2017/04/10/~/media/ECG/VirtualizationReview/Images/2016/11/1116vrm_openo_architecture.png

## Slide 50
Open Networking Ecosystem
Open Source vs. Commercial Solutions
Hardware
Programmable Data Plane
Network Controllers
Carrier Networking Functions
Virtual Machines
Operating Systems
Containers
VM/VI Managers
Application Platforms
Programming Frameworks
Network Switch OS
Management & Orchestration
Open Source
Commercial

## Slide 51
Open Networking Ecosystem
A simple scenario for Open Networking Ecosystem
  Phase 1 – Infrastructure building & NFV Development
Network Switch
Edge Cloud
Virtual Machines
OS
VM/VI Managers
Application Platforms
Frameworks
Firewall
DPI
Billing
IDS
Cache
OCP Switch H/W
P4 ASIC
Data Plane
Switch OS

## Slide 52
Open Networking Ecosystem
A simple scenario for Open Networking Ecosystem
  Phase 2 – Network & Service Configuration
Client
Datacenter
Firewall
DPI
Network Controller
Network Functions
Orchestration

## Slide 53
SDN/NFV Use Cases

## Slide 54
SDN/NFV Use Cases
ONOS CORD (Central Office Re-architected as a Datacenter)
  Key idea
    To concentrate distributed central offices to a re-architected datacenter
  Goal
    To construct cost-effective network by reducing CAPEX/OPEX
    Fast & flexible service provisioning
  Building blocks
    Commodity hardware
    ONOS, OpenStack/Kubernetes, XOS, vOLT, vSG, vRouter, vG.Fast, …
Commodity Hardware
(White-Box Servers and Switches, I/O Blades)

## Slide 55
SDN/NFV Use Cases
Aether
  Key idea
    To construct open source 5G connected edge platform for distributed enterprise networks
  Goal
    To provide mobile connectivity and edge cloud services
    E2E network slicing
  Building blocks
    Commodity hardware
    SD-Fabric/RAN (ONOS, P4/INT, Stratum, …), SD-CORE (4G/5G components)

## Slide 56
SDN/NFV Use Cases
Pronto
  Key idea
    To build and develop a connected edge cloud by leveraging network programmability
  Goal
    To provide secure & reliable network functionality
    Deep and wide network visibility, verification, and closed-loop control
  Building blocks
    Commodity hardware
    Based on Aether platform
Fine-Grained Network Telemetry
Verifier
High-level
specification
Closed-loop
control

## Slide 57
SDN/NFV Forum, Conferences & Journals

## Slide 58
ONF (Open Networking Foundation)
Non-profit organization promoting SDN, founded in 2011
Funded by service providers such as AT&T, China Unicom, Comcast, Deutsche Telekom, Google, NTT Communications, SK Telecom, Verizon, and vendors such as Cisco, Ericsson, Huawei, Nokia, Samsung, Intel, etc. (currently over 150 members companies)
Standardized the OpenFlow protocol
Offers product and skills certifications
  OpenFlow® Conformance Testing Program
  ONF-Certified SDN Professional Program (OCSP)
Recently merged with Open Networking Lab (ON.Lab)
Led by Guru Parulkar, Executive Director

## Slide 59
SDN/NFV Forum (http://www.sdnnfv.org)
Founded on Oct. 1, 2014 in Korea

## Slide 60
NetSoft (https://site.ieee.org/netsoft-2016/)
New IEEE conference focusing on “Network Softwarization”
NetSoft 2016 (June 6-10, 2016)
  7 keynote speakers, 57 technical papers
  250 attendees (http://sites.ieee.org/netsoft-2016/)
General Chair
  Prof. James Won-Ki Hong
Workshops
  SDN and IoT
  Open-Source Software Networking (OSSN)
  Software Defined 5G Networks (Soft5G)
  Security in Virtualized Networks (Sec-VirtNet)
Tutorials
  Smart Applications on Virtual Infrastructure (SAVI)
  NFV Management and Orchestration in the Age of 5G
  P4
  Central Office Re-architected as a Data Center (CORD)
  Powering Internet of Things with Cloud and NFV
  Software Defined Network Security – In Practice
NetSoft 2015 (London, UK, Apr. 13-17, 2015) (http://sites.ieee.org/netsoft-2015/) , NetSoft 2017 (Bologna, Italy, July 3-7, 2017) (http://sites.ieee.org/netsoft-2017/)
NetSoft 2018 (Montreal, Canada, June 25-29, 2018) (http://netsoft2018.ieee-netsoft.org/), NetSoft 2019 (Paris, France, June 24-28, 2019) (https://netsoft2019.ieee-netsoft.org/)
NetSoft 2020 (29 June-3 July 2020 // Virtual) (https://netsoft2020.ieee-netsoft.org/), NetSoft 2021 (28 June–2 July 2021 // Virtual) (https://netsoft2021.ieee-netsoft.org/)
NetSoft 2022 (27 June–1 July 2022 // Milan, Italy) (https://netsoft2022.ieee-netsoft.org/) NetSoft 2023 (19-23 June 2023 // Madrid, Spain) (https://netsoft2023.ieee-netsoft.org/)

## Slide 61
IJNM
International Journal of Network Management
  Publisher: Wiley, UK from 1990
  Editor-in-Chief: Prof. James Won-Ki Hong
  Impact Factor: 1.914, SCI(E)
  https://onlinelibrary.wiley.com/journal/10991190
Keywords
  SDN/NFV
  IoT management
  5G network management
  Mobile network management
  Telecommunications networks
  Network & service management
  Network monitoring and analysis
  Network security
Virtual Issue (free!)
  http://onlinelibrary.wiley.com/journal/10.1002/(ISSN)1099-1190/homepage/VirtualIssuesPage.html

## Slide 62
Concluding Remarks
Urgent need to reduce CAPEX & OPEX by Telcos
Need for more flexible, agile, efficient infrastructure to reduce time-to-market of new services & to be competitive
SDN/NFV (Open Networking, Network Softwarization) is a promising approach
Most telcos will NOT acquire proprietary HW/SW (e.g., middleboxes) any more
5G & 6G will be based on SDN/NFV for the infrastructure
SDN/NFV is a promising area to study, research & develop!

## Slide 63
Q & A

## Slide 64
Appendix

## Slide 65
Glossary
BSS: Business Support Systems
OSS: Operations Support Systems
GSR: Gigabit Switch Router
ACR: Access Control Router
RAS: Radio Access Station
vOLT: virtual Optical Line Terminal
vSG: virtual Subscriber Gateway
RRU: Remote Radio Unit
BBU: BaseBand Unit
SON: Self-Organizing Networks
GPON: Gigabit Passive Optical Network
ONT: Optical Network Terminal
PCE: Path Computation Element
MSPP: Multi Service Provisioning Platform
OXC: Optical Cross-Connect
PTN: Packet Transport Network
RNE: Radio Network Elements
CNE: Core Network Elements
FuAg: Function Agent
SE: Switching Elements
RAT: Radio Access Technology
MBH: Mobile BackHaul
MFH: Mobile FrontHaul
FQAM: Frequency & Quadrature Amplitude Modulation
SCMA: Sparse Code Multiple Access
NOMA: Non-Orthogonal Multiple Access
SOMA: Semi Orthogonal Multiple Access
D2D: Device To Device
eMTC: enhanced Machine-Type Communication

## Slide 66
References (1/2)
Hardware
  P4 – http://p4.org
    P4 Introduction/Tutorial 2016 – http://www.eventbrite.com/e/p4-introductiontutorial-2016-tickets-23066146465
    P4 Workshop 2016 – https://www.eventbrite.com/e/p4-workshop-2016-tickets-22712549848
  OCP - http://www.opencompute.org/
Network Switch Operating Systems
  ONL - https://opennetlinux.org/
  OpenSwitch – http://www.openswitch.net/
  Indigo - https://github.com/floodlight/indigo
Programmable Data Plane Services
  DPDK - http://dpdk.org/
  FD.io - https://fd.io/
  Open vSwitch - http://openvswitch.org/
Network Controllers
  ONOS - http://onosproject.org/
  OpenDaylight - https://www.opendaylight.org/
Carrier Networking Functions
  OPNFV - https://www.opnfv.org/
SDN/NFV Use cases
  CORD - https://opennetworking.org/cord/
  Aether - https://opennetworking.org/aether/
  Pronto - https://opennetworking.org/pronto-project/

## Slide 67
References (2/2)
Operating Systems
  Linux - http://www.linuxfoundation.org/
  FreeBSD - https://www.freebsd.org/
Virtual Machines
  Xen – http://www.xenproject.org/
  KVM - http://www.linux-kvm.org/page/Main_Page
Containers
  Docker - https://www.docker.com/
VM/VI Managers
  Kubernetes - http://kubernetes.io/
  OpenStack - https://www.openstack.org/
  Mesos - http://mesos.apache.org/
Management & Orchestration
  Open O - https://www.open-o.org/
  OSM - https://osm.etsi.org/, http://sdn.ieee.org/newsletter/july-2016/opensource-mano
  ONAP - https://www.onap.org/
Application Platforms
  Cloud Foundry - https://www.cloudfoundry.org/
  OpenShift - https://www.openshift.com/
Programming Frameworks
  Node.js - https://nodejs.org/en/
  Django - https://www.djangoproject.com/