## Slide 1: OCP: Open Rack
Seonyeong Heo
Dept. of CSE, POSTECH
heosy@postech.ac.kr
2016. 9. 27

## Slide 2: Outline
What is Open Rack?
Why Create an Open Rack Standard?
  Problems in the Traditional Rack Design
Implementation of Open Rack
References

## Slide 3: What is Open Rack?
Open API for Racks

## Slide 4: What is Open Rack?
The first rack standard designed for data centers
Timeline
  Open Rack Standard V1.0: released in 2013
  Open Rack Standard V2.0: under review
Facebook is the main contributor
Project Chairs
  Steve Mills (Facebook)
  Brian Obernesser (Fidelity Investments)

## Slide 5: Background: Traditional Rack Design
The EIA 310-D Specification (The 19” Rack Standard)
  Established in 1950s by EIA
  Designed for railroad signaling relays
  Standardize the width between the inner rails
Problems
  Lots of variations in server and rack design
  Unsuitable for data centers and scale computing

## Slide 6: Why Create an Open Rack Standard?
To Define the Mechanical and Electrical Interfaces between the Rack and the IT Gear
  Create Interoperability between Rack and IT Gear manufacturers
  Retain flexibility for innovation
  Optimize designs for large scale deployment
  Reduce development and deployment cost and cycle time

## Slide 7: Implementation: Top View
Open Rack includes three zones
  A cable zone
    face the cool-aisle side of data center
    manage and protect data cables
    technicians can add and remove equipment easily
  An equipment bay
    where equipment sits (e.g. servers, storage and switches)
  A power and cooling zone
    face the hot-aisle side of data center
    include one or more pairs of 12V bus bars
    include rack-level cooling fans
Hot-aisle of the data center
Cool-aisle of the data center
Air Flow

## Slide 8: Implementation: Assembly
OpenU
  A rack unit for Open Rack
  Slightly taller (48mm) than the traditional rack unit (44.5mm)
Advantage
  Increase airflow, improving air economization
  Better for cable and thermal management
Support ½ OpenU increments also
46U Rack
= 2.21m Rack
48mm

## Slide 9: Mechanical Requirements
Rack Columns
  Include rectangle holes
  Rectangle repeats every 48 mm = OpenU
IT Support Shelves
  Support equipment as small as 1 OpenU tall
Bus Bars
  Located in the back of the rack
  Transmit the 12V power
  Include a cover for protecting people
Rack Column
IT Support Shelve
Bus Bar

## Slide 10: Other Requirements
Electrical Requirements
  Bus Bar Electrical Specifications
  Bus Bar Power Connection
  IT Gear
    Hot Swap
    Noise Limits
    Max Power Draw
  Power Shelf

## Slide 11: If You Want More Details...
A 3D CAD file is available at GitHub.
Also, you can download the standard document at the OCP wiki website.
FRONT VIEW
BACK VIEW

## Slide 12: References
http://www.opencompute.org/blog/introducing-the-open-rack/
http://www.opencompute.org/wiki/Open_Rack
Open Rack Standard V1.0, Facebook, August, 2013
Community Update Slides, OCP Open Rack Engineering Submit, San Jose, 13 August, 2013
Introduction to Facebook Open Rack V2, OCP Open Rack Engineering Submit, San Jose, March, 2016